## Slide 1: SEEP2D
CE 544 – BRIGHAM YOUNG UNIVERSITY

## Slide 2: Background
2D finite element flow model
Written by Fred Tracy
US Army Engineer Waterways Experiment Station

## Slide 3: Applications
Suited for
Heterogeneous , anistropic soil properties
Confined/unconfined flow for profile models
Saturated/unsaturated flow for unconfined profile models
Confined flow for plan (areal) models
Axisymmetric models
Not suited for
Transient (time varying) problems
Unconfined plan models
Transport

## Slide 4: Governing Equation
Where:
H = total head
K = hydraulic conductivity

## Slide 5: Modeling Process
Model conceptualization/boundary conditions
Mesh generation
Analysis options
Material properties

## Slide 6: 1. Model Conceptualization
Determine model type
  Plan vs. Profile
  Confined vs. Unconfined
Determine appropriate boundary conditions

## Slide 7: Confined Flow, Ex. 1

## Slide 8: Confined Flow, Ex. 2

## Slide 9: Unconfined, Dupuit Problem

## Slide 10: Unconfined, Embankment

## Slide 11: Impermeable Barriers

## Slide 12: Impermeable Barriers, cont.

## Slide 13: 2. Mesh Construction
3 node triangles
4 node quadrilaterals

## Slide 14: 3. Analysis Options

## Slide 15: Unconfined Problems
Flow is modeled in both saturated and unsaturated zones
Phreatic surface is where pressure head = zero
Unsaturated Zone
Saturated Zone
Phreatic Surface

## Slide 16: Unsaturated Zone
where
H = total head
hp = pressure head
hel = elevation head
hp < zero in unsaturated zone

## Slide 17: Relative Conductivity
In unsaturated zone
where:
k = k used in unsaturated zone
kr = relative conductivity
ks = saturated conductivity

## Slide 18: Methods for Determining Kr
Linear front method
Van Genuchten method
Required parameters: kro, hmin
where a and m are empirical parameters based on soil type
** Default method **

## Slide 19: 4. Material Properties