## Slide 1: Slope Stability Charts
CE 544 – BRIGHAM YOUNG UNIVERSITY

## Slide 2: Chart Solutions
See Appendix in text
Can be used to solve for critical FS for a variety of simple problems
Simple and accurate solution for homogenous slopes, especially f=0 conditions
Can be used as approximation for non-homogenous cases by averaging strengths and unit weights

## Slide 3: f=0 Charts
See Figures A-1, A-2, A-3, A-4 in text
Assumes homogenous conditions
Adjustments provided for:
  Surcharge
  Submergence
  Tension crack (with or without water)

## Slide 4: Parameters

## Slide 5: Equations
General Case:
Non-submerged slope, no adjustments:
No comes from Figure A-1, pg 275
Adjustment factors mq, mw, and mt are associated with surcharge (q), submergence (Hw) and tension crack (Ht) and come from Figures A-2, A-3, A-4

## Slide 7: Location of Circles
Cotb < ~0.6 (b > 60o)
Critical circle does not pass below elevation of toe of slope, regardless of the depth of the foundation
“Toe Circle”

## Slide 8: Location of Circles
Cotb > ~0.6 (b < 60o)
Critical circle is tangent to base of slope and exit point is above the top of the slope.
“Slope Circle”
Presence of stronger materials prevents circle from penetrating below the base of the slope

## Slide 9: Location of Circles
0.6 < Cotb < 0.75 (53o < b < 60o)
Critical circle does not pass beyond the toe of the slope but may pass below the elevation of the toe.
“Toe Circle”
Presence of stronger materials at depth may affect outcome. See next slide.

## Slide 10: Location of Circles
0.75 < Cotb < 1 (45o < b < 53o)
Critical circle may pass through the toe of the slope or to the bottom of the foundation.
There may be two circles with minimum FS.
“Toe Circle” or “Deep Circle”

## Slide 11: Location of Circles
Cotb > 1.0 (b < 45o)
Critical circle passes to bottom of foundation, regardless of depth
“Deep Circle”

## Slide 12: Multiple Materials