## Slide 1: Important Details of Stability Analysis
CE 544 – BRIGHAM YOUNG UNIVERSITY

## Slide 2: Summary
Location of critical circles, local minima
Tension in the active zone
Forces in the passive zone

## Slide 3: Location of Critical Circles
Important details of stability analysis

## Slide 4: Location of Critical Surfaces
Automatic searches can often lead to local minima
The critical surface found is dependent on the location of the initial trial surface
Knowledge of the typical location of critical surfaces helps to guide the selection of initial trial surfaces

## Slide 5: Infinite Slope
Cohesionless soils (c=0 or c’=0)
  Critical surface is in layer with lowest f value.
Purely cohesive soils
  Critical surface is at depth with lowest ratio of c/z.
Multi-layer soils
  Check at the bottom of each layer

## Slide 6: Circular Surfaces
Cohesionless soils (c=0 or c’=0)
  Critical solution corresponds to infinite slope solution
  F=tanf/tanb

## Slide 7: Circular Surfaces, cont.
Purely cohesive soils (f = 0)
  Steep slopes (b>53o)
    See guidelines in stability chart slides
  Mild slopes
    Circles goes to bottom of layer
    Center point located in middle of slope

## Slide 8: Circular Surfaces, cont.
f = 0

## Slide 9: General Case

## Slide 10: Recommended Strategy
Select a starting location for the circle center using guidelines on previous slide(s)
For circle radius
  Try a toe circle
  Try a circle tangent to the bottom of each of the soil layers

## Slide 11: Non-Circular Surfaces – Starting Locations
General case (typical soil layering)
  Find critical circular surface
  Add points along circular surface
  Search for critical non-circular surface
Cases with thin, weak zones
  Starting surface should coincide to weak zone

## Slide 12: Multiple Minima – Special Cases
See “multi-min” exercise
Notes: See spreadsheet inputs. Work through the problem in UTEXASED with the two starting circles shown.
One min will be infinite slope solution. The other min will be deep circle with slightly larger FS. Which is the critical cirlce?
The deep circle is more critical since it would be much more costly to repair. The inf slope solution just requires a simple cosmetic fix.

## Slide 13: Tension in the Active Zone
Important details of stability analysis

## Slide 14: Tension in the Active Zone
  Soils cannot withstand tension – including tension leads to unconservative results

## Slide 15: Sample

## Slide 16: Rankine Active Earth Pressures
Depth of tension crack can be found:
Applicable to soils at crest of slope.
Slope stability case has some differences:
  a) Side forces are not always horizontal
  b) Strength may not be fully mobilized (F>1)
Notes: Figure in the book (14.9) has a typo.

## Slide 17: Negative Stresses, MC-Envelope
Negative stresses (s3) can occur on lower part of MC-envelope.
Although this makes sense for the purpose of defining a failure envelope equation, it does not mean that the soil can withstand tension.

## Slide 18: Causes of Tension
Tension can appear in limit equilibrium computations in three different ways
  Interslice forces become negative
  Normal forces (total or effective) on base of slice become negative
  Line of thrust moves outside the slice

## Slide 19: Line of Thrust
The line of thrust is at an infinite distance above or below slope at the point where the compressive forces balance the tensile forces.
The line of thrust is the location of the resultant interslice normal force. Calculated as:
Where Fi = resultant force from upper and lower triangle

## Slide 20: Eliminating Tension
Two approaches
  Use a modified (non-linear) MC failure envelope that does not allow shear strength when the normal stress becomes negative
  Add a tension crack

## Slide 21: Modified Strength Envelope
Caution: Discontinuity in slope can lead to numerical instability in slope stability software

## Slide 22: Modified Strength Envelope

## Slide 23: Tension Crack

## Slide 24: Tension Crack, cont.
(see exercise)

## Slide 25: Forces in the Passive Zone
Important details of stability analysis

## Slide 26: Inappropriate Forces in Passive Zone (toe of slope)
Under certain conditions, resultant force on base of slice may become either very large or negative
Happens when the resultant force at the base of the slice becomes very close to the direction of the interslice force

## Slide 27: Problems
Trial and error solution for FS may not converge
Forces may become extremely large and produce unreasonably high shear strengths in frictional materials
Forces may become negative (tensile)
UTEXAS output will give you warning messages when this problem occurs

## Slide 28: Solutions
Change the slip surface inclination (use non-circular surface)
Use OMS
Change the side force inclination (use a force equilibrium method)